## Slide 1: LELEC2350-Electromagnetic Waves
Presentation on Simulation of fields penetrating two slabs with normal incidence
Group Member:
Carbonnelle Gautier
Chowdhury Kamrul
Professor:
Craeye Christophe

## Slide 2: Simulation of fields penetrating two slabs with variable incidence angle
Declaring variables
  Define space (1D or 2D) and time grid
  Position slabs
  Spectrum initialization at z=0
Update wavevectors and reflection and transmission coeffs for given theta
  Complex impedances (TE and TM)
  Complex wavevectors (Snell’s law revisited for complex case)
  Complex reflection and transmission coefficients (TE and TM)
From Gamma at last interface, work way back to z=0
# Calculate Gamma at z=0, function of (freqs)
Gamma *= 0
for (k, l, r) in zip(
[wave vectors along z],
[positions of the interfaces],
[complex reflection coefficients (TE and TM modes)]):
Gamma = exp(-2j*k*l) * (r + Gamma) / (1 + r*Gamma)

## Slide 3: Simulation of fields penetrating two slabs with normal incidence
# Calculate 4 forward (A) and backward (B) fields at the start of each interface,
# function of (freqs)
B[0] = A[0] * Gamma
for i, (k, l, r, t) in enumerate(zip(
[wavevectors along z],
[positions of the interfaces],
[complex reflection coefficients],
[complex transmission coefficients])):
A[i+1] = 1/t * exp(-1j*k*l) * A[i] + r/t * exp(1j*k*l) * B[i]
B[i+1] = r/t * exp(-1j*k*l) * A[i] + 1/t * exp(1j*k*l) * B[i]
# Calculate waves to the right (E_r) and to the left (E_l) using wave function,
# function of (z, freqs)
z_i = 0
for i, k in enumerate([wavevectors along z]):
E_r[z_i: z_ip1] = A[i] * exp(-1j*z_local[i]*k)
E_l[z_i: z_ip1] = B[i] * exp(1j*z_local[i]*k)
z_i += len(z_local[i])

## Slide 4: Simulation of fields penetrating two slabs with normal incidence
Perform an FFT to get the time domain fields
# Perform IFFT on E_r, E_l
# function of (z, time)
if self.is_2D:
x_delay = exp(-2j*omega*c * k_slab_along_x * x)
else:
x_delay = 1.
x_delayed_spect = x_delay * spect
for E in [TM and TE, left and right E-fields]):
E = ifft(E * x_delayed_spect)