## Slide 1: LELEC2350-Electromagnetic Waves
Presentation on Simulation of fields penetrating two slabs with normal incidence
Group Member:
Carbonnelle Gautier
Chowdhury Kamrul
Professor:
Craeye Christophe

## Slide 2: Simulation of fields penetrating two slabs with normal incidence
Declaring variables
  Define space and time grid
  Position slabs
  Spectrum initialization at z=0
From Gamma at last interface, work way back to z=0
# Calculate Gamma at z=0, function of (freqs)
Gamma *= 0
for (k, l, r) in zip(
[k_s, k_0, k_s, k_0],
[d4 - d3, d3 - d2, d2 - d1, d1],
[r_s, r_0, r_s, r_0]):
Gamma = np.exp(-2j*k*l) * (r + Gamma) / (1 + r*Gamma)

## Slide 3: Simulation of fields penetrating two slabs with normal incidence
# Calculate 5 forward (A) and backward (B) fields at the start of each z_local,
# function of (freqs)
B[0] = A[0] * Gamma
for i, (k, l, r, t) in enumerate(zip(
[k_0, k_s, k_0, k_s],
[d1, d2 - d1, d3 - d2, d4 - d3],
[r_s, r_0, r_s, r_0],
[t_s, t_0, t_s, t_0])):
A[i+1] = 1/t * np.exp(-1j*k*l) * A[i] + r/t * np.exp(1j*k*l) * B[i]
B[i+1] = r/t * np.exp(-1j*k*l) * A[i] + 1/t * np.exp(1j*k*l) * B[i]
# Calculate waves to the right (E_r) and to the left (E_l) using wave function,
# function of (freqs, z_local)
z_i = 0
for i, k in enumerate([k_0, k_s, k_0, k_s, k_0]):
E_r[z_i: z_i+len(z_local[i])] = A[i] * np.exp(-1j*np.outer(k, z_local[i])).T
E_l[z_i: z_i+len(z_local[i])] = B[i] * np.exp(1j*np.outer(k, z_local[i])).T
z_i += len(z_local[i])
Perform an FFT to get the time domain fields